## Slide 1
Concrete Remaining Life Prediction
Yi-Leng Chen
Feb 2, 2024

## Slide 2
CONTENTS
  Introduction
  Goal statement
  Input and Output
  Assumption
  Equation
  Example of calculation

## Slide 3
INTRODUCTION
1
In 1992, a laboratory in the United States published a paper [1] which emphasizing the importance of predicting the remaining life of concrete structures.
[1] Building and fire research laboratory. (1992). Methods for Predicting Remaining Life of Concrete in Structures.https://nvlpubs.nist.gov/nistpubs/Legacy/IR/nistir4954.pdf
[2] Avalon_Studio.(2011). Construction workers smooth the concrete stock photo [Online image].iStock.https://www.istockphoto.com/photo/construction-workers-smooth-the-concrete-gm186821913-17024671

## Slide 4
GOAL STATEMENT
1
This project aims to develop a program that implements the theories, with the goal of predicting the remaining service life of concrete structures.
2

## Slide 5
INPUT AND OUTPUT
Input
Output
Parameters related to concrete
Remaining service life of the concrete
3

## Slide 6
EQUATION
Ad = kd ty n
4
Ad : Accumulated deterioration at time ty (years)
kd : Factors influencing deterioration
ty : Service life of concrete
n : Time order
Rd : Rate of degradation
Amount of concrete degradation
Rate of concrete degradation
Rd = n kd ty n-1

## Slide 7
EQUATION
4
tyf : Time to failure
Adf : Amount of damage at failure
tr : Remaining service life of concrete
ti : Age of the concrete at the time of condition inspection
Calculate the time to get failure
tyf = (Adf / kd)1/n
Remaining service life
tr = tf -ti

## Slide 8
EQUATION
4
Table 1. Values of n Obtained from Models

## Slide 9
The values of kd remain constant throughout the entire deterioration period.
The only factor influencing the remaining life of concrete and causing degradation is listed in Table 1.
Disregard self-conditions of concrete, such as cover thickness.
Unless specifically mentioned, consider multiple degradation processes occurring simultaneously, making the time order n=1.
If only one degradation process occurs, implicitly refer to Table 1 to determine the exact value of n.
All information obtained from inspections is accurate.
ASSUMPTIONS
5
Notes: Carbonation, sulfate attack

## Slide 10
EXAMPLE OF CALCULATION
6
If the average depth of carbonation was 24 mm after 36 years and the average concrete cover over the reinforcing bars was 48 mm
144-36=108(predicted remaining service life)

## Slide 11
Questions?